Byte 0: Always 0x1B
Byte 1: Always 0x84
Byte 2: Always 0x70
Byte 3:
Bit	Inverted	Function
0		Segment 0: A
1	Yes	Segment 0: F
2		Segment 0: E
3	Yes	Minus sign (-)
4		Diode sign
5		?
6		REL
7		?

Byte 4:
Bit	Inverted	Function
0	Yes	Segment 1: A
1		Segment 1: F
2	Yes	Segment 1: E
3		Dot between Segment 0 and 1
4		Segment 0: B
5		Segment 0: G
6	Yes	Segment 0: C
7		Segment 0: D

Byte 5:
Bit	Inverted	Function
0	Yes	Segment 2: A
1	Yes	Segment 2: F
2		Segment 2: E
3		Dot between Segment 1 and 2
4		Segment 1: B
5		Segment 1: G
6		Segment 1: C
7	Yes	Segment 1: D

Byte 6:
Bit	Inverted	Function
0		Segment 3: A
1		Segment 3: F
2	Yes	Segment 3: E
3	Yes	Dot between Segment 2 and 3
4		Segment 2: B
5		Segment 2: G
6	Yes	Segment 2: C
7		Segment 2: D

Byte 7:
Bit	Inverted	Function
0		?
1	Yes	Celsius
2	Yes	Fahrenheit
3		?
4		Segment 3: B
5		Segment 3: G
6		Segment 3: C
7	Yes	Segment 3: D

Byte 8:
Bit	Inverted	Function
0		Nano symbol for Farad
1	yes	Micro symbol for Farad
2	yes	Micro symbol for Farad
3		Farad
4	yes	trueRMS
5	yes	%
6	yes	Min
7		Max

Byte 9:
Bit	Inverted	Function
0	yes	Ampere
1		DC
2	yes	Milli symbol for volts
3		V
4	yes	Mega symbol for Ohms
5		Kilo symbol for Ohms
6	yes	Ohms
7		Hz

Byte 10:
Bit	Inverted	Function
0		?
1		?
2		?
3		?
4	yes	Milli symbol for Amps
5		Micro symbol for Amps
6		?
7	yes	Auto